| PART 1 - GENERAL |  |
| --- | --- |
| 1.1 RELATED SECTIONS | .1 03 20 01 - Concrete Reinforcement .2 03 30 01 – Cast-in-place Concrete .3 03 35 01 – Concrete Finishing |
| 1.2 REFERENCES | .1 Canadian Standards Association (CSA International) .1 CSA A23.1-09/A23.2-09, Concrete Materials and Methods of Concrete Construction/Methods of Test and Standard Practices for Concrete. .2 CSA O86S1-05, Supplement No. 1 to CSA O86-09, Engineering Design in Wood. .3 CSA O121-08, Douglas Fir Plywood. .4 CSA O151-09, Canadian Softwood Plywood. .5 CSA O153-M1980(R2008), Poplar Plywood. .6 CSA O325-07, Construction Sheathing. .7 CSA O437 Series-93(R2001), Standards for OSB and Waferboard. .8 CSA S269.1-1975(R2003), Falsework for Construction Purposes. .9 CAN/CSA-S269.3-M92(R2008), Concrete Formwork, National Standard of Canada .2 Underwriters' Laboratories of Canada (ULC) .1 CAN/ULC-S701-05, Standard for Thermal Insulation, Polystyrene, Boards and Pipe Covering. |
| 1.3 SUBMITTALS | .1 Submittals in accordance with Section 01 33 00 - Submittal Procedures. .2 Prepare shop drawings for formwork and falsework for review by the Consultant. .3 Indicate method and schedule of construction, shoring, stripping and re-shoring procedures, materials, arrangement of joints, special architectural exposed finishes, ties, liners, and locations of temporary embedded parts. Comply with CSA S269.1, for falsework drawings Comply with CAN/CSA-S269.3 for formwork drawings. .4 Indicate formwork design data: permissible rate of concrete placement and temperature of concrete in forms. .5 If required by the Consultant, indicate sequence of erection and removal of formwork/falsework. |
| 1.4 DELIVERY, STORAGE AND HANDLING | .1 Specify packing, shipping, handling, storage and protection for prefabricated forming to prevent any damage. |
| 1.5 WASTE MANAGEMENT AND DISPOSAL | .1 Separate waste materials for reuse, recycling and disposal in accordance with Section 01 74 19 – Construction Waste Management and Disposal. |
| PART 2 - PRODUCTS |  |
| 2.1 MATERIALS | .1 Select materials and resources in accordance with Section 01 47 13 – LEED Requirements. .2 Select reusable formwork systems were possible to reduce waste generation. .3 Consultant to specify material requirements for formwork including, but not limited to, the following, as applicable: .1 For architectural concrete surfaces. .2 For standard concrete surfaces. .3 Rigid insulation board. .4 Pan forms. .5 Tubular column forms. .6 Form ties. .7 Form release agent. .8 Falsework. .9 Sealants. .10 Chamfer and fillet forming. |
| PART 3 - EXECUTION |  |
| 3.1 FABRICATION AND ERECTION | .1 Fabricate and erect falsework in accordance with CSA S269.1 and CAN/CSA-S269.3. .2 Consider all exposed concrete as architectural concrete. .3 The Consultant to provide acceptable procedures and criteria as required for concrete formwork including, but not limited to, the following: .1 Architectural exposed finishes. .2 Chamfers and fillets. .3 Joint pattern and tie layout. .4 Build-in anchors, sleeves, and other inserts required in other Sections. .5 Cleaning formwork. .6 Re-use of formwork. .7 Removal and re-shoring. |