| PART 1 - GENERAL |  |
| --- | --- |
| 1.1 SECTION INCLUDES | .1 Performance criteria for weather tight roofing system Roofing System AVB, Insulation and Weather membrane Associated flashings and sealants Sealing and flashing for all penetrations and junctions Quality Control requirement .2 Related Sections: |
| 1.2 RELATED SECTIONS | .1 Division 1 |
| 1.3 STANDARDS | .1 Canadian Roofing Contractor’s Association (CRCA). .2 Comply with applicable ULC, local authority having jurisdiction requirements for Class A, fire resistant roof system. .3 Underwriters Laboratories of Canada (ULC) .1 Fire Resistance List of Equipment and Materials. .4 NBC 2010 |
| 1.4 DESIGN AND PERFORMANCE REQUIREMENTS | .1 Design components / assemblies to comply with requirements for “Post Disaster” buildings. .2 This project shall be designed and constructed in accordance with Section 01 47 13, LEED Requirements. .3 Performance: watertight roof system. .4 Insulation Requirement; RSI 5.28 (R 30) .5 Air tightness Requirement: 0.01 L/M²/S |
| 1.5 QUALITY ASSURANCE | .1 Conduct pre-installation meeting |
| 1.6 WARRANTY | .1 Warranty for Water tightness: 10 years. .2 Sheet Metal Roofing Components: Warranty for colour fastness - 20 years. |
| PART 2 - PRODUCTS |  |
| 2.1 ACCEPTABLE PRODUCTS | .1 Roof Membrane: .1 2-ply modified bituminous roofing system , or .2 Standing-seam prefinished metal roofing system. .2 Interior Finish: .1 Pre-finished metal or galvanized liner paneling. |
| PART 3 - EXECUTION |  |
| 3.1 INSTALLATION | .1 Install Roofing Systems |
| 3.2 QUALITY CONTROL | .1 Air Barrier –Leakage Tests: Provide ASTM certified leakage tests on air/vapour barrier/penetration junctions – minimum (4) per Streets / bridge garage component, minimum (4) per Administration component, minimum (4) per Parks garage component, Log results and submit to Quality Assurance representative daily. |
| 3.3 COMMISSIONING | .1 Verify fit, finish and performance compliance |