| PART 1 - GENERAL |  |
| --- | --- |
| 1.1 SECTION INCLUDES | .1 .1 Performance criteria for Acoustic Tile Ceiling Finish Systems. .2 Performance criteria for Drywall Ceiling Finish Systems |
| 1.2 RELATED SECTIONS | .1 Division 01 |
| 1.3 STANDARDS | .1 Fire-resistance rated floor/ceiling and roof/ceiling assembly: certified by Canadian Certification Organization, accredited by Standards Council of Canada. .2 American Society for Testing and Materials International (ASTM) .1 ASTM C 636current, Standard Practice for Installation of Metal Ceiling Suspension Systems for Acoustical Tile and Lay-In Panels. .2 ASTM C 840-current Specification for Application and Finishing of Gypsum Board. |
| 1.4 DESIGN & PERFORMANCE REQUIREMENTS | .1 Design components / assemblies to comply with requirements for “Post Disaster” buildings. .2 This project shall be designed and constructed in accordance with Section 01 47 13, LEED Requirements. .3 Construct ceiling finishes as parts of assemblies reflecting requirements for fire and acoustic separations .4 Ceiling system must, when installed in environment established, be sound, rigid, durable and properly related to the building structure. It must maintain specified dimensional tolerances and be free of deformation, de-lamination, and/or discolouration during service life. .1 Accessibility: .1 For a suspended modular unit paneled ceiling, accessibility is required to be at every panel. Removal and replacement must be effected without special tools and without damage to panels or to suspension system. .2 Sound Transmission Ratings: .1 Elevator Shafts: STC 57 .2 Meeting / conference Area: STC 55 .3 Offices / Washrooms; STC 50 .4 Garage Office Demising: STC 55 .3 Fire Containment/Prevention: .1 As required by NBC |
| 1.5 QUALITY ASSURANCE | .1 Execute the work with personnel experienced and familiar with systems of this type |
| PART 2 - PRODUCTS |  |
| 2.1 ACOUSTIC TILE CEILING SYSTEMS | .1 Provide acoustic tile ceiling system which matches, closely, in form, pattern texture and colour, following examples: .1 600 x 600 or 600 x 1200 mm grid, using 24 mm tee system and matching wall moulding. .2 600 x 600 or 600 x 1200 mm acoustic panel with beveled edge. .3 Colour: white |
| 2.2 DRYWALL CEILING SYSTEMS | .1 Provide suspended drywall ceiling system comprised of galvanized furring channels, wire hangers and drywall finishing – type as necessitated by rating requirements |
| PART 3 - EXECUTION |  |
| 3.1 INSTALLATION | .1 Install Ceiling Systems |
| 3.2 COMMISSIONING | .1 Verify fit, finish and compatibility |