| PART 1 - GENERAL |  |
| --- | --- |
| 1.1 SECTION INCLUDES | .1 Interior Painting: Wall, Doors, Ceilings, Doors & Frames, Stair components .2 Exterior Painting: Doors, Trim, Flashings |
| 1.2 RELATD SECTIONS | .1 Master Painters Institute (MPI) Architectural Painting Specifications Manual. .2 Test Method for Measuring Total Volatile Organic Compound Content of Consumer Products, Method 24 (for Surface Coatings) of the Environmental Protection Agency (EPA). .3 National Fire Code of Canada. |
| 1.3 STANDARDS | .1 Materials (primers, paints, coatings, varnishes, stains, lacquers, fillers, thinners, solvents, etc.) shall be in accordance with MPI Painting Specification Manual "Approved Product" listing and shall be from a single manufacturer for each system used. .2 Other paint materials such as linseed oil, shellac, turpentine, etc. shall be the highest quality product of an approved manufacturer listed in MPI Painting Specification Manual and shall be compatible with other coating materials as required. . .3 Standard of Acceptance: .1 Walls: No defects visible from a distance of 1000 mm at 90° to surface. .2 Ceilings: No defects visible from floor at 45° to surface when viewed using final lighting source. .3 Final coat to exhibit uniformity of colour and uniformity of sheen across full surface area. .1 Walls: Eggshell .2 Ceilings: Flat .3 Doors: Semi-gloss .4 Frames: Semi-gloss |
| 1.4 DESIGN & PERFORMANCE REQUIREMENTS | .1 Design components / assemblies to comply with requirements for “Post Disaster” buildings. .2 This project shall be designed and constructed in accordance with Section 01 47 13, LEED Requirements. .3 Submit product data in accordance with Section 01 33 00 - Submittal Procedures. |
| 1.5 QUALITY ASSURANCE | .1 Contractor shall have a minimum of five years proven satisfactory experience .2 Qualified journeymen who have a "Tradesman Qualification Certificate of Proficiency" shall be engaged in painting work. Apprentices may be employed provided they work under direct supervision of a qualified journeyman in accordance with trade regulations. .3 Conform to latest MPI requirements for painting work including preparation and priming. |
| 1.6 SITE REQUIREMENTS | .1 Temperature, Humidity and Substrate Moisture Content Levels: .1 Unless specifically pre-approved by the specifying body, Paint Inspection Agency and the applied product manufacturer, perform no painting work when: .1 Ambient air and substrate temperatures are below 10 ° C for both interior and exterior work. .2 Substrate temperature is over 32 ° C unless paint is specifically formulated for application at high temperatures. .3 Substrate and ambient air temperatures are expected to fall outside MPI or paint manufacturer's prescribed limits. .4 Relative humidity is above 85 % or when dew point is less than 3 ° C variance between air/surface temperature. .5 Rain or snow are forecast to occur before paint has thoroughly cured or when it is foggy, misty, raining or snowing at site. .2 Perform no painting work when maximum moisture content of substrate exceeds: .1 12 % for concrete and masonry (clay and concrete brick/block). .2 15 % for wood. .3 12 % for plaster and gypsum board. .3 Conduct moisture tests using a properly calibrated electronic Moisture Meter, except test concrete floors for moisture using a simple "cover patch test". .4 Test concrete, masonry and plaster surfaces for alkalinity as required. .2 Surface and Environmental Conditions: .1 Apply paint finish in areas where dust is no longer being generated by related construction operations or when wind or ventilation conditions are such that airborne particles will not affect quality of finished surface. .2 Apply paint to adequately prepared surfaces and to surfaces within moisture limits noted herein. .3 Apply paint when previous coat of paint is dry or adequately cured. |
| PART 2 - PRODUCTS | .1 Paint interior surfaces in accordance with MPI Architectural Painting Specification Manual requirements for materials |
| PART 3 - EXECUTION |  |
| 3.1 INSTALLATION | .1 Paint unfinished surfaces |
| 3.2 COMMISSIONING | .1 Verify finish and thickness |