| - GENERAL |  |
| --- | --- |
| SECTION INCLUDES | This Section outlines the materials, construction and installation requirements for chain link fences and gates, including motorized sliding gates, as per CW 3550, Chain Link Fencing and Drawing 01-C-4001 – Motorized Sliding Gate Miscellaneous Details and Cross Sections. |
| CITY SPECIFICATIONS, | CW 3550 - Chain Link Fencing. |
| SUBMITTALS | Submittals in accordance with Section 01 33 00 - Submittal Procedures. Coordinate submittal requirements and provide submittals required by Section 01 47 13 - LEED Requirements. Closeout submittals as per Section 01 78 00. |
| PART 2 - PRODUCTS |  |
| 2.2 MATERIALS | Concrete mixes and materials: in accordance with CW 3550, Section 5.11. Additives: fly ash to CAN/CSA-A23.5. Chain-link fence fabric: in accordance with CW 3550, Section 5.6. Chain link gates: as per CW 3550, Section 9.7. Provide motorized sliding gates at two main vehicular entrances, two in each location, as per details on Drawing 01-C-4001. Motorized sliding gates shall be Card Access controlled. Provide Shop Drawings for motorized sliding gates showing construction details. Organic zinc rich coating: to CAN/CGSB-1.181. Galvanizing: For chain link fabric: to CAN/CGSB-138.1 Grade 2. For pipe: 550g/m² minimum to ASTM A 90. For other fittings: to CAN/CSA-G164. .6 Grounding rod: 16mm diameter copperwell rod, 3 m long. |
| PART 3 - EXECUTION |  |
| 3.1 GRADING | .1 Remove debris and correct ground undulations along fence line to obtain smooth uniform gradient between posts. .1 Provide clearance between bottom of fence and ground surface of 30mm to 50mm. |
| 3.2 ERECTION OF FENCE | .1 Erect fence in accordance with CW 3550, Section 9. .2 Install end posts at ends of fence and at buildings, and on both sides of gate openings. .3 Install grounding rods. |
| 3.3 INSTALLATION OF GATES | Install gates in locations as indicated on the Conceptual Site Drawings. Level ground between gate posts and set gate bottom approximately 40mm above ground surface. Install 1.2 metre high bollards, depth to prevent frost heaving, to protect gate and latch portal when the gate is open. Locate bollards on either side of the Card Access reader/intercom pedestal (two at each pedestal) for protection of pedestal. Install gate stops. |
| 3.4 OPERATIONAL REQUIREMENTS | .1 Operational requirements in accordance with Section 01 74 11 – Cleaning. |
| 3.5 TOUCH UP | Clean damaged surfaces with wire brush removing loose and cracked coatings. Apply two coats of organic zinc-rich paint to damaged areas. Pre-treat damaged surfaces according to manufacturers' instructions for zinc-rich paint. |
| 3.6 CLEANING | Clean and trim areas in compliance with CW 3550, Section 9.9 |