| - GENERAL |  |
| --- | --- |
| 1.1 SECTION INCLUDES | This Section includes outline specifications for materials and installation of standard manufactured catalogue items including: benches, picnic tables, waste containers, and bicycle storage system. |
| 1.2 REFERENCES AND RELATED SECTIONS | .1 Canada Green Building Council (CaGBC) LEED® Green Building Rating System – LEED® Canada-NC Version 1. |
| SUBMITTALS | .1 Submit product data in accordance with Section 01 33 00 - Submittal Procedures. .2 Submit Shop Drawings in accordance with Section 01 33 00 - Submittal Procedures. Indicate dimensions, sizes, assemblies, anchorage and installation details for each furnishing specified. .3 Provide maintenance data for care and cleaning of site furnishings for incorporation into manual specified in Section 01 78 00 - Closeout Submittals. .4 Section 01 74 13 - LEED Requirements |
| - PRODUCTS |  |
| 2.1 BENCHES AND PICNIC TABLES | Locate benches at least 8 m from building entrances, opening windows and air intakes. Locate picnic tables in hard surfaced areas accessible to entrances in the Administrative and Staff component building. Acceptable Materials: recycled plastic or metal. Dimensions: Lengths of benches and picnic tables: min. 1.83 m. |
| 2.2 TRASH CONTAINER | .1 Provide minimum of four (4) trash containers, near benches and picnic tables, and major building entrances. .2 Acceptable Material: recycled plastic or metal to match benches. |
| 2.3 ASH URNS | .1 Provide ash urns with each trash container. .2 Acceptable Materials: to match trash containers. |
| 2.4 BICYCLE RACKS | .1 Provide secure and covered bicycle storage to accommodate at least 5% of building occupants (12 bicycles or more). .2 Acceptable Material: recycled wood or metal. |
| - EXECUTION |  |
| 3.1 INSTALLATION | Assemble furnishings in accordance with manufacturer's instructions. Install furnishings true, plumb, anchored to hard surfacing. Touch-up damaged finishes. |