| - GENERAL |  |
| --- | --- |
| DESCRIPTION | .1 This Section outlines requirements for topsoil, topsoil amendments, and growing medium, as well as the stripping of topsoil, should viable topsoil exist on site; the preparation of existing grades, placing of topsoil and finish grading. |
| SITE MATERIAL | .1 Ensure that suitability and usefulness of on-site material is checked and verified by a certified professional or Soil Testing Laboratory. |
| 1.3 REFERENCES AND RELATED SECTIONS | City of Winnipeg Standard Construction Specifications: .1 CW 3170 – Earthwork and Grading .2 CW 3540 – Topsoil and Finish Grading .2 Related Sections .1 Section 31 32 19_01 – Geotextiles .2 Section 32 92 16 - Hydraulic Seeding .3 Section 32 92 23 - Sodding .4 Section 32 93 10 - Trees Shrubs and Ground Cover Plantings. .5 Section G1030 - Site Earthwork |
| REFERENCES | .1 CW 3540 Topsoil and Finish Grading for Establishment of Turf Areas. |
| SUBMITTALS | Provide submittals in accordance with Section 01 33 00 - Submittal Procedures. Submit Erosion and Sedimentation Control Plan in accordance with Section 01 47 13 LEED Requirements. Quality control submittals: .1 Soil testing: submit certified test reports showing compliance with specified performance characteristics and physical properties. .2 Certificates: submit product certificates signed by manufacturer certifying materials comply with specified performance characteristics and criteria and physical requirements. |
| - PRODUCTS |  |
| TOPSOIL | Topsoil for areas to receive Grass Seed Mixture: shall be either stockpiled site soil or imported topsoil, as per CW 3540. Planting Soil Mixture for planting beds and tree pits: mixture of 70% topsoil with 20% peat moss and 10% sand by volume. |
| GROWING MEDIUM | .1 Peat moss and sand constituents of Growing Medium for areas to receive Legume and Grass Seed Mixture: as per CW 3540. .2 Compost shall be unrestricted grade: includes yard, agricultural and silvicultural wastes plus untreated wood products that have been treated by pathogen-free requirement procedures (PFRP), that is, maintained at 131°F (55°C) for 48 to 96 hours. This treatment ensures that the compost is free of disease-causing organisms. |
| 2.3 SOIL AMENDMENTS 2.4 MULCH | Contractor is responsible for amendments to supply topsoil as specified. Soil testing by recognized testing facility for PH, P and K, and organic matter. .1 Mulch shall be clean river run stone, 20mm to 30mm. |
| - EXECUTION |  |
| 3.1 TEMPORARY EROSION AND SEDIMENTATION CONTROL | Provide temporary erosion and sedimentation control measures to prevent soil erosion and discharge of soil-bearing water runoff or airborne dust to adjacent properties and walkways, according to sediment and erosion control plan, specific to site, that complies with EPA 832/R-92-005 or requirements of authorities having jurisdiction, whichever is more stringent. Inspect, repair, and maintain erosion and sedimentation control measures during construction until permanent vegetation has been established. Remove erosion and sedimentation controls and restore and stabilize areas disturbed during removal. |
| STRIPPING OF TOPSOIL | As per CW 3540 Strip topsoil to depths as determined by localized soil depth and chemistry testing. |
| 3.3 PREPARATION OF EXISTING GRADE | Prepare existing grade in accordance with Section G1030 – Site Earthwork. |
| 3.4 PLACING AND SPREADING OF TOPSOIL/PLANTING SOIL | Place and spread topsoil in accordance with CW 3540. For sod areas: spread topsoil to a minimum depth after settlement of 100 mm. .3 For planting beds: spread planting soil mixture to a minimum depth after settlement of 300 mm. .4 For infiltration trenches spread minimum of 750 mm of prepared planting medium. .5 Manually spread topsoil/planting soil around trees, shrubs and obstacles. |
| SOIL AMENDMENTS | .1 For sod and seeded grass areas: apply and thoroughly mix soil amendments as recommended by soil test results into top 50mm of existing soil: .2 For planting beds and infiltration trenches: apply and thoroughly mix soil amendments as recommended by soil test results into full specified depth of soil mixture. |
| GROWING MEDIUM 3.7 VEGETATED INFILTRATION TRENCHES 3.8 FINISH GRADING | .1 For areas to receive Legume and Grass Seed Mixture: mix 35 mm peat moss and 15 mm sand into the top 75 mm of clean clay cover, following construction of rough grades. .1 Prepared planting medium for vegetated infiltration trenches: shall include a mixture of 30% topsoil, 50% sand and 20% compost .2 Gravel underdrain blanket: for the entire width of the infiltration swale shall extend 300 mm from minimum the 200 mm perforated sub-drain discharge pipe connected to the on-site stormwater system. .3 Filter fabric: shall be installed between prepared planting medium and gravel underdrain blanket. .4 Install river-run stone to 50mm depth around all plantings. .1 Finish grading as per CW 3540. |
| 3.9 ACCEPTANCE | .1 Test topsoil for NPK to determine fertilizer requirements and application rates. |
| 3.10 SURPLUS MATERIAL | Dispose of materials, except imported topsoil not required, off site. |
| CLEANING | .1 Proceed in accordance with Section 01 74 11 – Cleaning. |