| - GENERAL |  |
| --- | --- |
| DESCRIPTION | .1 This Section outlines requirements for hydraulic seeding including seed, mulch, slurry preparation and application, and maintenance. .1 Grass Seed Mixture: typically used in boulevard and higher maintenance landscaped areas, such as around the parking lot and in swales. .2 Legume and Grass Seed Mixture: typically used in undeveloped and low-maintenance landscaped areas, including slopes of stormwater retention pond. |
| RELATED SECTIONS | Section 31 31 19.13 - Chemical Control of Vegetation. Section 32 91 19.13 - Topsoil Placement and Grading. Section G1030 - Site Earthwork |
| 1.3 SUBMITTALS | Submit product data in accordance with Section 01 33 00 - Submittal Procedures, for seed mix, mulch, tackifier and fertilizer |
| 1.4 SCHEDULING | .1 Schedule hydraulic seeding to coincide with preparation of soil surface, between dates recommended by the Provincial Agricultural Department for seeding grasses and legumes. |
| 1.5 WASTE MANAGEMENT AND DISPOSAL | .1 Divert unused fertilizer from landfill to official hazardous material collections site. .2 Do not dispose of unused fertilizer into sewer systems, lakes, streams, onto ground or in locations where it will pose health or environmental hazard. |
| - PRODUCTS |  |
| MATERIALS | .1 Grass Seed Mixture: for boulevards, medians and lake areas, as per CW 3520, Section 5.3.2., or alternate native seed mix comprising three or more hardy, native grasses appropriate to site conditions. .2 Legume and Grass Seed Mixture: "Canada No. 1" in accordance with Government of Canada "Seeds Act" and "Seeds Regulations". .1 Mixture composition: .1 Birdsfoot trefoil 35%. .2 White Clover 25%. .3 Perennial ryegrass 15% cultivars as per CW 3520, Section 5.3.4. .4 Creeping Red fescue 25% or alternate seed mix comprising two or more hardy native legumes and two or more hardy native grass species appropriate to site conditions. .3 Mulch, Tackifier and Water: as per CW 3520. .4 Fertilizer: .1 To Canada "Fertilizers Act" and "Fertilizers Regulations". .2 Complete synthetic, slow release fertilizer with 35% of nitrogen content in water-insoluble form. |
| - EXECUTION |  |
| WORKMANSHIP | As per CW 3520. |
| 3.2 PREPARATION OF SURFACES | .1 As per Section 32 92 20 - Topsoil and Finish Grading. .2 Cultivate areas to receive the Legume and Grass Seed Mixture to a depth of 75 mm. .1 Mix 35 mm of peat moss and 15 mm sand with clean clay base. .3 Ensure areas to be seeded are moist to depth of 100 mm before seeding. |
| 3.3 FERTILIZING PROGRAM | .1 As per Section 31 92 20. |
| 3.4 PREPARATION AND APPLICATION OF SLURRY | .1 As per CW 3520 |
| 3.5 MAINTENANCE DURING ESTABLISHMENT PERIOD | .1 As per CW 3520. .2 For legume and grass seed mixtures intended for periodic mowing, only. Mow legume mixtures to 100 mm whenever height reaches 200 mm and as follows: Do not mow within period commencing 3 weeks before and ending 3 weeks after first severe, average fall frost date and 3 weeks after actual severe fall frost. .2 When mowing after first severe fall frost, mow at a height of not less than 300 mm. .3 Remove clippings which will smother plants. .3 Water all seeded areas during establishment period to maintain optimum soil moisture level for germination and continued growth. Control watering to prevent washouts. |
| 3.6 ACCEPTANCE | .1 As per CW 3520. |
| 3.7 MAINTENANCE DURING WARRANTY PERIOD | .1 Perform following operations from time of acceptance until end of warranty period: .1 Repair and reseed dead or bare spots. .2 Mow areas seeded, remove clippings, in accordance with following schedule: |

Seed             		Frequency Requirements       	Height of

Mixture           		for                                         	Cut

Cutting	  ____________________________

Turf Grass       		Bi-weekly        			60 mm

Legume mixture  	Periodically height of 200 mm  	100 mm   _

|  | .3 Fertilize seeded areas as per Section 31 92 20. |
| --- | --- |
| 3.8 CLEANING | .1 As per CW 3520. |