| PART 1 – GENERAL |  |
| --- | --- |
| 1.1 SUMMARY | .1 This Section outlines requirements for the supply and installation of watermain distribution piping, fittings, hydrant assemblies, valves, water services, connections to existing watermains, valve relocations, hydrant relocations, appurtenances, testing, restorations and related work. |
| 1.2 DEFINITIONS | .1 Municipal Service: shall refer to infrastructure installed and constructed for the purposes of delivering potable water to the proposed site, including all piping, fittings, valves, hydrants, and related appurtenances. .2 Building Service: shall refer to the water distribution branch providing water service directly to and entering the footprint of the proposed building. |
| 1.3 REFERENCES AND RELATED SECTIONS | .1 City of Winnipeg Standard Construction Specifications .1 CW 2110 – Watermains .2 City of Winnipeg Standards and Guidelines for the Mitigation of Methane Gas at Buildings and Utilities AND Guidelines for Construction on Landfill Sites. .3 Related Sections .1 01 33 00 – Submittal Procedures. .2 01 74 19 – Construction Waste Management And Disposal. .3 31 23 33.01 – Excavating, Trenching and Backfilling. |
| 1.4 PERFORMANCE REQUIREMENTS | .1 Work shall be performed in accordance with CW 2110 – Watermains. .2 The design shall include methods and specifications intended to achieve acceptable performance as the site settles, and help minimize future maintenance requirements. .3 The design shall consider the chemical and physical effects of fill materials present at the site on the integrity of the municipal services. .4 In order to minimize the potential for underground gas migration within excavations and trenches, buried municipal services shall be installed in a common trench system wherever possible. .5 Locate watermains, valves, hydrants, services, and related appurtenances to minimize the impact of trench settlement on surface features. .6 Minimize the number of offsite watermain connections to: .1 Reduce the impact of service interruptions to existing users. .2 Minimize the requirement for installation of gas barriers and trench gas migration plugs. .7 Service connections to buildings shall be constructed such that .1 Differential settlement between the service and the structural slab floor does not negatively impact the integrity, operation or performance of the utility. .2 Any utility or conduit entering through the floor shall be sealed to prevent infiltration of methane gas into the building. |
| 1.5 SUBMITTALS | .1 Submit designs, shop drawings, plans and details in accordance with Section 01 33 00 - Submittal Procedures. .2 Prior to beginning excavation submit for approval by the Contract Administrator, plans, drawings and documentation in support of: .1 Plan/Profile drawings clearly indicating pipe alignments, depth, grades, pipe size, class, material, and any other information pertinent to the design of the water distribution piping system. .2 Indicate trench/excavation type (i.e. open-cut, trenchless), bedding classes, and location of trench gas barriers. .3 Design and detail drawings for watermain distribution piping appurtenances, including building service connection details. .3 Testing, laboratory results, and quality control documentation shall be made available to the Contract Administrator upon request. |
| 1.6 QUALITY ASSURANCE | 1 Sustainable Requirements: .1 Contractor shall perform work in accordance with: .1 Section 01 47 13 – LEED Requirements. .2 Section 01 74 19 – Construction Waste Management and Disposal. |
| PART 2 – PRODUCTS |  |
| 2.1 MATERIALS | .1 Materials and products in accordance with CW 2110 – Watermains. .2 Valves to open counter clockwise (right hand close), with a black operating nut, as per City of Winnipeg Standard Construction Specifications SD-008. .3 Pipe bedding and backfill to be installed in accordance with Section 31 23 33.01 – Excavating, Trenching and Backfilling. .4 Pipe gaskets to be oil and gas resistant, and elastomeric compounds to be rated as “excellent”. |
| PART 3 - EXECUTION |  |
| 3.1 INSTALLATION | .1 Do trenching work in accordance with Section 31 23 33.01 - Excavating Trenching and Backfilling. |