| PART 1 - GENERAL |  |
| --- | --- |
| 1.1 SUMMARY | .1 This Section shall outline requirements for removal from the site of trees, stumps, roots, logs, brush, rubbish, debris, concrete, asphalt, refuse, surface litter and materials described above, and the disposal of same in a manner specified within this document. |
| 1.2 CITY SPECIFICATIONS, RELATED SECTIONS AND REFERENCES | .1 City of Winnipeg Standard Construction Specifications: .1 CW 1130 – Site Requirements .2 CW 3010 – Clearing and Grubbing. .2 Related Sections: .1 01 33 00 - Submittal Procedures. .2 01 47 13 – LEED Requirements .3 01 74 19 - Construction Waste Management and Disposal .3 Canada Green Building Council (CaGBC) LEED® Green Building Rating System – LEED® Canada-NC Version 1.0. |
| 1.3 DEFINITIONS | .1 Site Work: Shall cover examination of existing site features, dewatering and site drainage, clearing and grubbing, materials management, waste management, and site cleanup. |
| 1.4 PERFORMANCE REQUIREMENTS | .1 Site work will be performed in accordance with CW 1130 – Site Requirements. .2 Clearly define limits of stripping and site clearing, topsoil stockpile areas, and waste material stockpile areas to minimize site disturbance outside of the intended construction area. .3 Perform clearing and grubbing in accordance with CW 3010 – Clearing and Grubbing, including removal and disposal of construction waste items consistent with the description in Part 1.1 – Summary, of this Section. .4 Maintain existing surface drainage to protect excavations, low areas, and depressions from flooding, rainfall, and surface run-off. .5 Do not direct drainage water from ground surface or excavations into existing sewer system without written approval from the Contract Administrator, and in accordance with local sewerage by-laws. |
| 1.5 SUBMITTALS | .1 Coordination of Submittals: In accordance with Section 01 33 00 - Submittal Procedures. .2 Prior to beginning work on site submit for approval by the Contract Administrator, plans, drawings and documentation in support of: .1 Schedule and staging of site clearing activities. .2 Stripping, clearing, and construction limits, indicating areas, objects, surface and sub-surface features which are to remain undisturbed or require protection during construction. .3 Material stockpile locations. |
| 1.6 QUALITY ASSURANCE | .1 Sustainable Requirements: .1 Design Builder Team shall perform work in accordance with: .1 Section 01 47 13 - LEED Requirements. .2 Section 01 74 19 - Construction Waste Management and Disposal. |
| PART 2 - PRODUCTS | .1 In accordance with City of Winnipeg Standard Construction Specifications CW 3010 – Clearing and Grubbing |
| PART 3 - EXECUTION |  |
| 3.1 PREPARATION | .1 Coordinate pre-construction activities in accordance with City of Winnipeg Standard Construction Specifications CW 1130 – Site Requirements. .2 Review site with Contract Administrator and verify items designated to remain. .3 Locate and protect utility lines: preserve in operating condition active utilities traversing site. .4 Notify utility authorities before beginning work to strip, clear or grub site. |
| 3.2 INSTALLATION | .1 Site clearing work in accordance with City of Winnipeg Standard Construction Specification CW 3010 – Clearing and Grubbing. |
| 3.3 RESTORATION | .1 Leave ground surface in a condition suitable for commencement of building construction and site construction operations. |
| 3.4 QUALITY CONTROL | .1 Verification requirements in accordance with: .1 Section 01 47 13 - LEED Requirements. .2 Section 01 74 19 – Construction Waste Management and Disposal and the Waste Management Plan (WMP). |
| 3.5 CLEANING | .1 Clean and reinstate areas affected by Work. .2 Keep pavement and area adjacent to site clean and free from mud, dirt, and debris at all times. .3 Objects removed from site to be managed in accordance with the Waste Management Plan (WMP). |