| PART 1 - GENERAL |  |
| --- | --- |
| 1.1 SUMMARY | .1 This Section outlines requirements for removal of existing site material and placement of clean fill materials required for the preparation of Yard and parking lot areas, as well as lake excavations, side slopes, and drainage works. |
| 1.2 CITY SPECIFICATIONS, RELATED SECTIONS AND REFERENCES | .1 City of Winnipeg Standard Construction Specifications: .1 CW 3110 – Sub-Grade, Sub-Base, and Base Course Construction. .2 CW 3170 – Earthwork and Grading .2 Related Sections: .1 01 33 00 - Submittal Procedures. .2 01 47 13 – LEED Requirements. .3 01 74 19 – Construction Waste Management and Disposal. .4 23 33.01 Excavation Trenching and Backfilling .5 G1010 – Site Clearing .3 Canada Green Building Council (CaGBC) LEED® Green Building Rating System – LEED® Canada-NC Version 1.0. |

| 1.3 DEFINITIONS | .1 Site Work: covers examination of existing site features, dewatering and site drainage, clearing and grubbing, materials management, waste management, and site cleanup. |
| --- | --- |

| 1.4 PERFORMANCE REQUIREMENTS | .1 Examine preliminary geotechnical soil report titled: Former Elmwood/ Nairn Avenue Landfill Site Final Preliminary Site Condition Assessment Report as prepared by KGS Group, located in Appendix D and other relevant reports/information located in Appendices B, C and D. .2 Design Build Team Engineering Consultant to: .1 Develop settlement projections intended to achieve acceptable performance as the site settles, and help minimize future maintenance requirements. .2 Incorporate rip-rap, retaining walls, engineered fill, hydraulic geotextile filters where steeper slopes are necessary to stabilize soil, protect slope and control erosion of final site contours. .3 Site earthwork shall be performed in accordance with CW 3170 – Earthwork and Grading. |
| --- | --- |
| PART 2 – PRODUCTS | .1 Materials and products in accordance with CW 3170 – Earthwork and Grading. |
| PART 3 - EXECUTION |  |
| 3.1 PREPARATION | .1 Prior to commencing earthwork and grading, the Design Build Team shall perform site clearing operations in accordance with Section G1010 – Site Clearing. |
| 3.2 EXCAVATION | .1 Excavation and placement operations shall be performed in accordance with CW 3170 – Earthwork and Grading. .2 Install dewatering system to keep sub-grade dry and convey groundwater away from excavations. .1 Maintain until de-watering is no longer required. .2 Outfall dewatering system to include an acceptable sediment trapping device, in accordance with Erosion Control Plan. |
| 3.3 BACKFILLING AND CONTOURING | .1 Backfilling and contouring activities shall be performed in accordance with City of Winnipeg Standard Construction Specification CW 3170 – Earthwork and Grading. |
| 3.4 FIELD QUALITY CONTROL | .1 Field quality control methods shall be performed in accordance with City of Winnipeg Standard Construction Specification CW 3170 – Earthwork and Grading. .2 Verification requirements shall be in accordance with Section 01 47 13 – LEED Requirements. |
| 3.5 CLEANING | .1 Clean and reinstate areas affected by the Work. .2 Keep pavement and area adjacent to site clean and free from mud, dirt, and debris at all times. |