| Form C(R1): Technical Specifications (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.1 - Basic Enterprise Desktop |
| Brand (HP, Dell, or Lenovo): |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| PC Case: Small Form Factor |  |  |
| CPU: Intel Core i3 or equivalent |  |  |
| RAM Memory: DDR3, 4 GB in 2*2GB |  |  |
| Graphics: integrated video, VGA D-sub or DVI-D Output |  |  |
| Network Interface:10/100/1000 GbE |  |  |
| Hard drive: 120GB SSD |  |  |
| Bays: 1 unused 5.25 Expansion Bays |  |  |
| Ports: 5 USB 2.0 Ports, 1 USB 3.0, Audio In/Out, Headphone and Mic |  |  |
| Mouse: Optical wheel, USB Connection |  |  |
| Keyboard: Standard US English, USB Connection |  |  |
| Audio: Integrated |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year onsite |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.2 - Standard Enterprise Desktop |
| Brand (HP, Dell, or Lenovo): |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| PC Case: Small Form Factor |  |  |
| CPU :Intel Core i5 or equivalent |  |  |
| RAM Memory: DDR3, 8 GB in 2*4GB |  |  |
| Graphics: Support dual displays. onboard Integrated video, VGA D-Sub or DVI-D output, 512 MB Shared video ram, Must be Windows compliant |  |  |
| Network Interface:10/100/1000 GbE |  |  |
| Hard drive: 120GB SSD |  |  |
| Bays: 1 unused 5.25 Expansion Bays 1 unused 3.5 expansion bay |  |  |
| Ports: 6 USB 2.0, 1 USB 3.0, display port, Audio In/Out, Headphone and Mic |  |  |
| Mouse: Optical wheel, USB Connection |  |  |
| Keyboard: Standard US English, USB Connection |  |  |
| Audio: Integrated |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year onsite |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.3 - Advanced Enterprise Desktop |
| Brand (HP, Dell, or Lenovo): |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| PC Case: Mini Tower |  |  |
| CPU: Intel Core i7 or equivalent |  |  |
| RAM Memory: DDR3, 16 GB in 2*8GB |  |  |
| Graphics: Support dual displays. VGA D-SUB+DVI-D or DVI-D+DVI-D, PCI-E addon card, 1024 MB dedicated Video RAM, AMD Firepro 4900 or equivalent. Must be Windows compliant |  |  |
| Network Interface:10/100/1000 GbE |  |  |
| Hard drive: 240 GB SSD |  |  |
| Bays: 2 unused 5.25 Expansion Bays 1 unused 3.5 expansion bay |  |  |
| Ports: 6 USB 2.0 Ports /2 USB 3.0 Audio In/Out, Headphone and Mic |  |  |
| Mouse: Optical wheel, USB Connection |  |  |
| Keyboard: Standard US English, USB Connection |  |  |
| Audio: Integrated |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year onsite |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.4 - Standard Laptop / Notebook |
| Brand: HP, Dell, Lenovo, Toshiba, Fujitsu, Microsoft |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| Screen: 15.6” resolution of 1366 X 768 |  |  |
| CPU: Intel Core i5 or equivalent |  |  |
| RAM Memory: DDR3, 8 GB |  |  |
| Graphics: HD Graphics |  |  |
| Hard drive: 120 SSD |  |  |
| Network Interface: 10/100/1000 GbE |  |  |
| Wireless: 802.11 a/b/g/n/ac and Bluetooth |  |  |
| Expansion Slots:1 media card reader |  |  |
| Ports and accessories: USB 3.0 1 USB 3.0 charging 1 DisplayPort or HDMI 1 VGA 1 combo stereo headphone/mic jack 1 integrated camera 1 integrated microphone 1 AC power 1 RJ-45 1 docking station |  |  |
| Battery: 6 hours with medium usage |  |  |
| Weight: as light as possible. Bidder to specify weight |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year onsite |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.5 - Advanced Laptop / Notebook |
| Brand: HP, Dell, Lenovo, Toshiba, Fujitsu, Microsoft |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| Screen: 15.6” resolution 1600 x 900 |  |  |
| CPU: Intel Core i7 or equivalent |  |  |
| RAM Memory: DDR3, 16 GB |  |  |
| Graphics: Intel HD Graphics |  |  |
| Hard drive: 120 SSD |  |  |
| Network Interface: 10/100/1000 GbE |  |  |
| Wireless: 802.11 a/b/g/n/ac and Bluetooth |  |  |
| Expansion Slots:1 multi format SD media card reader |  |  |
| Ports and accessories: USB 3.0 1 USB 3.0 charging 1 Display Port or HDMI 1RJ 45 1 combo stereo headphone/mic jack 1 integrated camera 1 integrated microphone 1 AC power 1 docking station |  |  |
| Battery: 6 hours with medium usage |  |  |
| Weight: as light as possible. Bidder to specify weight |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year onsite |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.6 - Standard Windows Tablet |
| Brand |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 downgrade to 8.1 |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| CPU: Intel Core i5 Processor or equivalent |  |  |
| Memory: 4 GB |  |  |
| Graphics: Intel HD Graphics or equivalent |  |  |
| Display: 12 to 13.5” touchscreen with 1920 x 1080 or higher resolution |  |  |
| Storage: 120 GB |  |  |
| Network Interface: Wi-Fi (802.11a/b/g/n/ac) |  |  |
| Ports: Full-size USB 3.0, microSDXC card slot, Headset jack |  |  |
| Keyboard: Detachable keyboard |  |  |
| Misc: Fanless, Bluetooth |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year onsite |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.7 - Advanced Windows Tablet |
| Brand |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 downgrade to 8.1 |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| CPU: Intel Core i7 Processor or equivalent |  |  |
| Memory: 8 GB |  |  |
| Graphics: Intel HD Graphics or equivalent |  |  |
| Storage: 240 GB |  |  |
| Network Interface: Wi-Fi (802.11a/b/g/n) |  |  |
| Ports: Full-size USB 3.0, microSDXC card slot, Headset jack, Mini DisplayPort, Cover port |  |  |
| Keyboard: Detachable keyboard |  |  |
| Misc: Fanless, Bluetooth |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.8 - Basic Monitor |
| Brand |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Panel Size/Type: 18.9" or 19” IPS, LED Backlit, 4:3 ratio or 5:4 ratio |  |  |
| Native Resolution: 1280x1024 or equivalent |  |  |
| Contrast Ratio: 1000:1 (static) |  |  |
| Brightness: 250 cd/m2 |  |  |
| Inputs: VGA, DVI-D, DisplayPort |  |  |
| Ergonomics: Tilt, Pivot Rotation, Swivel, Supports VESA MIS |  |  |
| Stand adjustments: Height adjustable |  |  |
| Misc: detachable power cord |  |  |
| Qualifications ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.9 - Standard Monitor |
| Brand |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Panel Size/Type: 23" IPS, LED Backlit, 16:9 ratio |  |  |
| Native Resolution: 1920x1080 |  |  |
| Contrast Ratio: 1000:1 (static) |  |  |
| Brightness: 250 cd/m2 |  |  |
| Inputs: VGA, DVI-D, DisplayPort |  |  |
| Ergonomics: Tilt, Pivot Rotation, Swivel, Supports VESA MIS |  |  |
| Stand adjustments: Height adjustable |  |  |
| Misc: detachable power cord |  |  |
| Qualifications ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section A: Common Office Equipment |
| A.10 - Advanced Monitor |
| Brand |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Panel Size/Type: 27" IPS, LED Backlit, 16:9 ratio |  |  |
| Native Resolution: 2560 x 1400 |  |  |
| Contrast Ratio: 1000:1 (static) |  |  |
| Brightness: 250 cd/m2 |  |  |
| Inputs: VGA, DVI-D, DisplayPort |  |  |
| Ergonomics: Tilt, Pivot Rotation, Swivel, Supports VESA MIS |  |  |
| Stand adjustments: Height adjustable |  |  |
| Misc: detachable power cord |  |  |
| Qualifications ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section B: Specialty Office Equipment |
| B.1 - Standard Thin Client |
| Brand |  |
| Application Name: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows Embedded Standard 7E or Windows 10 IoT Enterprise |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| CPU: AMD GX-212JC Dual-Core SOC APU(1.2 GHz) Or equivalent |  |  |
| Memory: 2GB DDR3 |  |  |
| Graphics: Integrated AMD Radeon HD Graphics or equivalent |  |  |
| Ports: VGA and 2 x DisplayPort, 2 USB 3.0, 4 USB 2.0, 1 headphone, 1 microphone |  |  |
| Network Interface: 10/100/1000 GbE |  |  |
| Supported Protocols: Citrix® ICA Citrix® HDX Microsoft RDP Microsoft RemoteFX (RFX) VMware Horizon View through RDP VMware Horizon View through PCoIP |  |  |
| Keyboard/Mouse: Wired USB |  |  |
| Audio: Internal amplified speaker |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section B: Specialty Office Equipment |
| B.2 - Advanced Thin Client |
| Brand |  |
| Application Name: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows Embedded Standard 7E 32 |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| CPU: AMD GX-217GA Dual-Core APU (1.65 GHz) or equivalent |  |  |
| Memory: 4GB DDR3 |  |  |
| Graphics: Integrated AMD Radeon HD 8280E or equivalent |  |  |
| Ports: VGA and 2 x DisplayPort, 2 USB 3.0, 4 USB 2.0, 1 headphone, 1 microphone |  |  |
| Network Interface: 10/100/1000 GbE |  |  |
| Supported Protocols: Citrix® ICA Citrix® HDX Microsoft RDP Microsoft RemoteFX (RFX) VMware Horizon View through RDP VMware Horizon View through PCoIP |  |  |
| Keyboard/Mouse: Wired USB’ |  |  |
| Audio: Internal amplified speaker |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section B: Specialty Office Equipment |
| B.3 - Fanless Nano PC |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional if possible |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| CPU: Intel Celeron N2930 quad core or equivalent |  |  |
| Memory: 8 GB |  |  |
| Graphics: Intel HD Graphics or equivalent - HDMI, DisplayPort |  |  |
| Hard drive: 120 SSD |  |  |
| Network Interface:1000Mbps, 802.11ac WiFi |  |  |
| Misc: Fanless, USB3, Bluetooth |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacture Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section B: Specialty Office Equipment |
| B.4 - Advanced Nano PC |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional if possible |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| CPU: Intel Core i7 - 5557U processor dual core with hyperthreading or equivalent |  |  |
| Memory: 16GB dual channel |  |  |
| Graphics: Iris Graphics 6100 or equivalent - Mini HDMI, Mini DisplayPort |  |  |
| Hard drive: 120 SSD |  |  |
| Network Interface: Intel PRO 10/100/1000, Intel Wireless 802.11ac |  |  |
| Misc: Fanless, USB3, Bluetooth |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: Manufacture Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section C: Specialty Field Equipment |
| C.1 - Semi-Ruggedized Laptop |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| Display: 14", 1366x768, touchscreen, Anti-glare and anti-reflective coating, Concealed (Night) mode setting |  |  |
| CPU: Intel Core i5 or equivalent |  |  |
| RAM Memory: DDR3, 8 GB |  |  |
| Graphics: HD Graphics |  |  |
| Audio/Camera: Integrated speakers, microphone and 1080P camera |  |  |
| Hard drive: 120GB SSD |  |  |
| Network Interface: RJ-45 10/100/1000 Ethernet |  |  |
| Wireless: 802.11 a/b/g/n/ac and Bluetooth v4.0 |  |  |
| Expansion Slots :1 multi format SD media card reader |  |  |
| Ports and accessories: USB 3.0 Micro SD Mini-jack stereo Option for smartcard reader Option for GPS Option for 4G LTE multi carrier broadband Docking station connector |  |  |
| Battery: 4 hours with medium usage |  |  |
| Weight: Bidder to specify |  |  |
| Rugged Certifications: IP51 MIL-STD-810G |  |  |
| Construction: metal case with handle |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section C: Specialty Field Equipment |
| C.2 - Standard Ruggedized Laptop |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 12 months with forty five (45) days’ notice of HAL changes. |  |  |
| Display: 10", 1024x768 touchscreen, Anti-glare and anti-reflective coating, Supports stylus |  |  |
| Keyboard: Chiclet style keyboard with individual key backlighting |  |  |
| Touchpad: Pressure/resistive touch pad for gloved touch capability |  |  |
| Audio: Integrated speakers and microphone |  |  |
| CPU: Intel Core i5 or equivalent |  |  |
| RAM Memory: DDR3, 4 GB |  |  |
| Hard drive: Shock mounted 120GB SSD |  |  |
| Network Interface: RJ-45 10/100/1000 Ethernet |  |  |
| Wireless: 802.11 a/b/g/n/ac Bluetooth v4.0, Embedded 4G cellular modem |  |  |
| Ports and accessories: USB 3.0, Docking station connector compatible with CF-19 docks, Mini-jack stereo, Option for Smartcard reader, Option for GPS, Option for Camera |  |  |
| Battery: 6 hours with medium usage |  |  |
| Weight: Bidder to Specify |  |  |
| Rugged Certifications: IP65, 3rd Party Tested MIL‐810G |  |  |
| Construction: Latched port covers, Raised Bezel |  |  |
| Mounting: Must be compatible with Gamber Johnson LLC NP CF18 series vehicle mounts |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year; Allow certification of City technicians |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section C: Specialty Field Equipment |
| C.3 - Advanced Ruggedized Laptop |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| Display: 13” 1024 x 768 sunlight viewable LED touchscreen, Anti-glare and anti-reflective coating, Concealed (Night) mode setting |  |  |
| Keyboard: Chiclet style keyboard with individual key backlighting |  |  |
| Touchpad: Pressure/resistive touch pad for gloved touch capability |  |  |
| CPU: Intel Core i5 or equivalent |  |  |
| RAM Memory: DDR3, 8 GB |  |  |
| Audio: Integrated speakers and microphone |  |  |
| Hard drive: 120GB SSD |  |  |
| Network Interface: RJ-45 10/100/1000 Ethernet |  |  |
| Wireless: 802.11 a/b/g/n/ac and Bluetooth v4.0 |  |  |
| Expansion Slots :1 multi format SD media card reader |  |  |
| Ports and accessories: USB 3.0, Micro SD, Mini-jack stereo, Option for smartcard reader, Option for GPS, Option for 4G LTE Multi Carrier, Broadband, Docking station connector |  |  |
| Battery: 4 hours with medium usage |  |  |
| Weight: Bidder to Specify |  |  |
| Rugged Certifications: IP65, MIL-STD-810G |  |  |
| Construction: Metal case with handle, latched port covers |  |  |
| Mounting: Must be compatible with Precision Mounting Technologies Ltd TrimLine CF-31 vehicle mounts |  |  |
| Qualifications: ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section C: Specialty Field Equipment |
| C.4 - Standard Ruggedized Tablet |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| Display: 10", 1024x768, capacitive touchscreen Anti-glare and anti-reflective coating Concealed (Night) mode setting Supports stylus |  |  |
| CPU: Intel Core i5 or equivalent |  |  |
| RAM Memory: DDR3, 4 GB |  |  |
| Audio: Integrated speakers and microphone |  |  |
| Hard drive: 120GB SSD |  |  |
| Network Interface: RJ-45 10/100/1000 Ethernet |  |  |
| Wireless: 802.11 a/b/g/n/ac and Bluetooth v4.0 |  |  |
| Expansion Slots :1 multi format SD media card reader |  |  |
| Ports and accessories: USB 3.0 Micro SD Mini-jack stereo Option for smartcard reader Option for GPS Docking station connector |  |  |
| Battery: 6 hours with medium usage |  |  |
| Weight: Bidder to specify |  |  |
| Rugged Certifications: IP65 Dust and water resistant MIL-STD-810G |  |  |
| Construction: Port covers Raised Bezel |  |  |
| Qualifications ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section C: Specialty Field Equipment |
| C.5 - Advanced Ruggedized Tablet |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Operating System: Hardware must support and include Windows 10 Professional downgradeable to Windows 7 Professional |  |  |
| Hardware consistency (see D4.1(d)): Model lifecycle of 6 months with forty five (45) days’ notice of HAL changes. |  |  |
| Display: 1900x1200 IPS capacitive multitouch, Anti-glare and anti-reflective coating Concealed (Night) mode setting Supports stylus |  |  |
| CPU: Intel Core i5 or equivalent |  |  |
| RAM Memory: DDR3, 8 GB |  |  |
| Audio: Integrated speakers and microphone |  |  |
| Hard drive: 120GB SSD |  |  |
| Network Interface: RJ-45 10/100/1000 Ethernet |  |  |
| Wireless: 802.11 a/b/g/n/ac and Bluetooth v4.0 |  |  |
| Expansion Slots :1 multi format SD media card reader |  |  |
| Ports and accessories: USB 3.0 Micro SD Mini-jack stereo Option for smartcard reader Option for GPS Docking station connector |  |  |
| Battery: 10 hours with medium usage |  |  |
| Weight: Bidder to Specify |  |  |
| Rugged Certifications: IP65 Dust and water resistant MIL-STD-810G |  |  |
| Construction: Port covers Raised Bezel |  |  |
| Qualifications ENERGY STAR® certified EPEAT® Silver level certification |  |  |
| Warranty: 3-year warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section C: Specialty Field Equipment |
| C.6 - Ruggedized Printer |
| Brand: | Datamax-O'neil |
| Model: | OC3 |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Media type: Direct thermal receipt paper |  |  |
| Connectivity: Bluetooth |  |  |
| Drop specification: 4ft |  |  |
| Fonts: User configurable |  |  |
| Print head: Direct thermal, 203 dpi |  |  |
| Accessories: IP54 soft case |  |  |
| Compatibility: Windows, Windows CE, DOS |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section C: Specialty Field Equipment |
| C.7 - Ruggedized Printer for Android |
| Brand: | Datamax-O'neil |
| Model: | Apex3 |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Media type: Direct thermal receipt paper |  |  |
| Connectivity: Bluetooth |  |  |
| Drop specification: 4ft |  |  |
| Fonts: User configurable |  |  |
| Print head: Direct thermal, 203 dpi |  |  |
| Accessories: IP54 soft case |  |  |
| Compatibility: Windows, Windows CE, DOS, Android |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section D: Uninterrupted Power Supply |
| D.1 - Basic UPS |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Type: Line-interactive |  |  |
| Sizes: 700, 1000, and 1500 VA, tower form factors. Bidder to specify price for each size |  |  |
| Network: built in Ethernet interface or an equivalent expansion card. |  |  |
| Rack mount kits. Bidder to specify pricing separately |  |  |
| Battery expansion modules. Bidder to specify pricing separately |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section D: Uninterrupted Power Supply |
| D.2 - Standard UPS |
| Brand: |  |
| Model: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Type: Online double-conversion, Eaton 9130 or equivalent |  |  |
| Sizes: 700, 1000, and 1500 VA, 19 inch rack mount or tower form factors. Bidder to specify prices for each available VA and form factor combination. |  |  |
| Network: Built in Ethernet interface or an equivalent expansion card. |  |  |
| Rack mount kits. Bidder to specify pricing separately |  |  |
| Battery expansion modules. Bidder to specify pricing separately |  |  |
| Warranty: Manufacturer Warranty |  |  |

| FORM C(R1): TECHNICAL SPECIFICATIONS (See B10) SUPPLY AND DELIVERY OF COMPUTER HARDWARE AND ACCESSORIES |
| --- |
| Section E: Endpoint Management |
| E.1 - Endpoint Management System |
| Brand |  |
| Application Name: |  |
| Minimum Specifications | Meets or Exceeds (Yes / No) | Explanation where specification not met or exceeded. |
| Hardware Inventory including tracking hardware changes and warranty period tracking |  |  |
| Software Inventory including tracking removed software |  |  |
| Software Deployment including third party patch deployment |  |  |
| Software Uninstall |  |  |
| Software Licensing/Subscription Management including Software Metering |  |  |
| Customizable reporting |  |  |
| Report scheduling |  |  |
| Customizable dashboard |  |  |
| Enterprise-level stability and robustness |  |  |
| Agent based information gathering |  |  |
| Be accessible by all City departments |  |  |
| Ability for a department’s desktop support staff to only see and control the devices owned by that department |  |  |
| Ability for each department to independently determine how they will use the system in their environment |  |  |